## Slide 1
BCSE308P COMPUTER NETWORKS LAB
Predictive Adaptive Mesh
Routing Protocol
Energy-Constrained IoT Networks
F2 Team 19
Siddhi Gulati 24BCE0817
Harshitha Nethi 24BCT0084
Saamiya Siddique 24BKT0146
Notes: Introduce the three team members. This is a custom Python simulation and dashboard. It does not implement a full wireless stack or standard RPL. The evaluation uses synthetic modeled energy.

## Slide 2
Problem and motivation
02
Sensors forward readings through neighboring relays to reach a gateway.
A heavily used relay can exhaust its battery and interrupt several sources.
Current battery level can hide a rapidly increasing drain rate.
Question: does forecasting energy improve next-hop selection?
Notes: Source: our simulator model and RFC 6550 background, https://www.rfc-editor.org/rfc/rfc6550.html. Explain sensors, relays, gateway, and why a relay affects upstream sources.

## Slide 3
Existing mechanisms and baseline gap
03
Mechanism | Useful idea | Question for this prototype
RPL and LLN metrics [1,2] | Rooted routing and node/link metrics | How should a forecast affect a local score?
MRHOF [3] | Hysteresis limits route churn | Can we stabilize forecast-driven switches?
Shortest-hop baseline | Minimum-hop progress | Repeated use can concentrate battery drain
Reactive baseline | Current energy, loss and queue | What additional benefit comes from prediction?
The contribution is an implemented comparison. Publication-level novelty has not been established.
Notes: Background: RFC 6550, https://www.rfc-editor.org/rfc/rfc6550.html; RFC 6551, https://www.rfc-editor.org/rfc/rfc6551.html; RFC 6719, https://www.rfc-editor.org/rfc/rfc6719.html. The two implemented baselines are custom controls, not standard RPL or MRHOF implementations.

## Slide 4
System architecture
04
Seeded topology
and scheduled traffic
Packet queues
and battery model
Local observations
and parent selection
Run history
and metrics
HTTP API
and dashboard replay
Same physical network and workload for all three strategies
Physical connectivity is a mesh. Forwarding follows one selected parent per sensor and strictly decreasing initial levels.
Notes: This is an editable algorithm architecture diagram, not a hardware deployment. The simulator has global state for execution and visualization. Parent choice reads local received observations. Initial BFS levels are centrally computed.

## Slide 5
Energy prediction with EWMA
05
drain = α × recent drain + (1 − α) × previous drain
future energy = max(0, energy − drain × (H + age))
Sample every 5 seconds. Advertise every 10 seconds.
Defaults: α = 0.35 and forecast horizon H = 40 seconds.
Recent consumption must remain informative over the horizon.
Advertisement age corrects an older energy sample. Abrupt load changes can make the forecast inaccurate.
Notes: Background: NIST/SEMATECH e-Handbook of Statistical Methods, Single Exponential Smoothing, https://www.itl.nist.gov/div898/handbook/pmc/section4/pmc431.htm. This implementation smooths recent energy drain, then linearly projects remaining energy. It does not train a neural network.

## Slide 6
Parent selection and loop prevention
06
Cost = 0.65 × energy risk
+ 0.20 × link loss + 0.15 × queue fraction
Eligible parents have a fresh advertisement and a lower initial BFS level.
Choose the lowest cost. Switch only if improvement exceeds 0.06.
Retain packets while no route exists, until TTL expires.
The reactive baseline uses current advertised energy. PAMR replaces it with estimated future energy.
Notes: Our cost is a local normalized score, not an accumulated end-to-end path metric. Strict decreasing initial levels prevent loops but exclude some post-failure detours. All terms are clamped to comparable ranges. Gateway eligibility is preferred.

## Slide 7
Worked routing example
07
Candidate | Energy now | Drain EU/s | Energy +40s | Predictive cost
Relay A | 80 EU | 0.90 | 44 EU | 0.4140
Relay B | 65 EU | 0.10 | 61 EU | 0.2985
Reactive energy prefers A. The forecast prefers B because its energy drains more slowly.
Example link success: A 0.90, B 0.85. Queues: A 4 packets, B 2 packets.
Notes: Illustrative arithmetic, not a trace quoted from experiments. Both capacities are 100 EU, advertisement age is zero, H=40 s, queue limit=20. Reactive cost prefers A (.1800 versus .2725). Predictive cost prefers B (.4140 versus .2985). The improvement .1155 exceeds hysteresis .06.

## Slide 8
Implementation setup
08
Python simulator with an HTML, JavaScript and SVG dashboard.
30 sensors and one powered gateway. Static positions, radius 32.
400 seconds per run. Queues hold 20 packets. TTL is 100 seconds.
Three attempts per current hop. Data TX/RX costs 0.10/0.05 EU.
Saved JSON configuration and topology files reproduce the default simulation without Packet Tracer.
Notes: Runtime dependencies: Python standard library only. Source: Config and Simulation in simulator.py, app.py, static/index.html. Energy units are illustrative. One-second service slots are not measured radio transmission times.

## Slide 9
Scenarios and performance metrics
09
Case | Base packet probability | Change
S1 / S2 / S3 | 0.015 / 0.030 / 0.060 | Low / medium / high steady load
S4 Burst | 0.030 | Triple probability in middle third
S5 Failure | 0.030 | Relay 1 forced offline at 200 s
Metrics: demand delivery, packet delivery, delay, energy per delivered packet, first battery death, route changes and forecast error.
Ten matched seeds per case. Report means and sample SD, with no-death observations censored at 400 seconds.
Notes: Source: experiments.py and results/experiments.csv. Five scenarios times ten matched seeds times three policies equals 150 runs. Use sample standard deviation. No formal significance test is claimed.

## Slide 10
Repeated-run delivery results
10
Steady load | Shortest-hop % | Reactive % | Predictive %
Low | 98.52 ± 0.84 | 98.61 ± 0.70 | 98.68 ± 0.80
Medium | 97.92 ± 1.21 | 98.22 ± 1.03 | 98.50 ± 0.64
High | 73.08 ± 3.46 | 74.82 ± 3.11 | 75.05 ± 2.42
At high load, prediction improves mean delivery by 1.97 percentage points relative to shortest-hop.
Notes: Actual means and sample SD from results/summary.json. Values are percent of all scheduled sensor readings, including unavailable source demand. The improvement beyond reactive routing is smaller than the gain relative to shortest-hop.

## Slide 11
Delivery across load levels
11
Chart: Scheduled readings delivered
| Low load | Medium load | High load
Shortest-hop | 0.98522 | 0.97925 | 0.73077
Reactive | 0.98614 | 0.98217 | 0.74817
Predictive | 0.98679 | 0.98499 | 0.7505
Mean differences are modest relative to some run-to-run variation. This chart does not establish statistical significance.
Notes: Source: results/summary.json, means over ten matched seeds per load. The chart displays means only. Sample SD is in the preceding table and report plots. Literal chart data are embedded for editability.

## Slide 12
Stress cases and a counterexample
12
Stress case | Shortest-hop % | Reactive % | Predictive %
Traffic burst | 73.26 ± 5.88 | 75.51 ± 5.03 | 75.85 ± 4.62
Relay failure | 79.15 ± 4.54 | 81.74 ± 4.31 | 81.83 ± 4.71
Seed 42 burst: predictive delivery is 80.94%, compared with 82.32% for reactive routing.
Prediction can improve an aggregate result while losing on a particular seed or another metric.
Notes: Source: results/summary.json and results/F2_Team19_Simulation.json. In repeated burst runs, predictive mean delay is 13.43 seconds versus 15.38 seconds for shortest-hop. The default seed-42 example is a separate run and shows why no universal improvement is claimed.

## Slide 13
Analysis and limitations
13
Idle and control costs dominate more strongly at low traffic.
High load exposes queue and gateway-adjacent relay bottlenecks.
Energy costs are synthetic. Link attempts ignore RF contention.
Fixed initial levels prevent loops but can block useful detours.
Fourteen automated checks pass. Real dashboard screenshot evidence must be captured on the presentation laptop.
Notes: Source: MODEL.md and actual experiments. No real RF, hardware calibration, or protocol compliance is claimed. Tests verify algorithm and accounting invariants, not the fidelity of a complete wireless network stack.

## Slide 14
Conclusion future work and references
14
A reproducible prototype shows conditional gains and explicit routing trade-offs.
Next: calibrated energy, realistic contention, distributed repair, and parameter sensitivity.
[1] Winter et al. RPL RFC 6550 2012
[2] Vasseur et al. LLN routing metrics RFC 6551 2012
[3] Gnawali and Levis MRHOF RFC 6719 2012
[4] NIST/SEMATECH Single Exponential Smoothing
Notes: References: [1] T. Winter et al., RPL, RFC 6550, March 2012, doi:10.17487/RFC6550. [2] J. P. Vasseur et al., Routing Metrics Used for Path Calculation in Low-Power and Lossy Networks, RFC 6551, March 2012, doi:10.17487/RFC6551. [3] O. Gnawali and P. Levis, MRHOF, RFC 6719, September 2012, doi:10.17487/RFC6719. [4] NIST/SEMATECH e-Handbook, Single Exponential Smoothing, https://www.itl.nist.gov/div898/handbook/pmc/section4/pmc431.htm. Live demo: run app.py, switch strategies, alter a parameter, inspect decisions, and explain actual results.